## Slide 1: Arduino workshop
WEBER LIU
05-03-2019

## Slide 2: Why are we using Arduinos?
Physiology research has always been dependent on developing and using tools/electronics!
  X-lab tools are plug-and-play
  If we needed to make our own tools, we wouldn’t be able to!
  Arduinos give us a new level of control in designing our own tools
    Bespoke individual solutions to problems
    Learn how to create and implement small electronic devices
    Learn how to program
We hope that after this lesson you will be more interested in electronics and programming

## Slide 3: What’s an Arduino?
Consider how our brain works
  Receptor (sensor) sends information in
  Brain processes information
  Effector performs function
Compare to how an Arduino circuit works
  Arduino acts as the information processor
  Pulse sensor acts as receptor
  LEDs act as effector
Image from: http://mammothmemory.net/biology/coordination-and-response/nerves/three-types-of-neurone.html

## Slide 4: Step 1a: Getting started
Collect Arduino sandwich bag from front – contains:
    Arduino Uno board
    Breadboard
    USB cable (to connect w/ PC)
    Pulsimeter
    10 pixel neopixels strip
    Short ‘jumper’ cable

## Slide 5: Step 1b: Wiring your Arduino
WTF is going on?

## Slide 6: Step 1b: Wiring your Arduino
WTF is going on?
The 5V and GND pins are powering the positive and negative rails respectively
The A0 pin is connected to the horizontal strip with the DATA PIN on the pulse sensor
The Digital 6 pin is connected to the horizontal strip with the DATA PIN on the ped

## Slide 7: 2. Arduino details
Pseudocode
“There’s an analogue sensor attached to pin A0”
“Whatever the sensor’s saying, put it in the variable ‘sensorValue’”
“Before you begin ANYTHING, make sure you’re sending any info from the sensor to the computer at 9600bps”
“Repeat the following commands:
  Read in the value from the analogInPin (pin A0) and save it into the variable ‘sensorValue’
  Send the variable ‘sensorValue’ over to the computer via the ‘Serial’
  Wait 100ms before repeating
“
Arduino code
const int analogInPin = A0;
int sensorValue = 0;
void setup() {
Serial.begin(9600);
}
void loop() {
sensorValue = analogRead(analogInPin);
Serial.println(sensorValue);
delay(100);
}

## Slide 8: 2. Arduino details (more detail)
Pseudocode
“There’s an analogue sensor attached to pin A0”
“Whatever the sensor’s saying, put it in the variable ‘sensorValue’”
“Before you begin ANYTHING, make sure you’re sending any info from the sensor to the computer at 9600bps”
“Repeat the following commands:
  Read in the value from the analogInPin (pin A0) and save it into the variable ‘sensorValue’
  Send the variable ‘sensorValue’ over to the computer via the ‘Serial’ … = perform a calculation on the ‘sensorValue’ and use the calculated value to light up a neopixels strip
  Wait 100ms before repeating
“
Arduino code
const int analogInPin = A0;
int sensorValue = 0;
void setup() {
Serial.begin(9600);
}
void loop() {
sensorValue = analogRead(analogInPin);
Serial.println(sensorValue);
…
delay(100);
}

## Slide 9: 2. Arduino details (more detail)
Pseudocode
“There’s an analogue sensor attached to pin A0”
“Whatever the sensor’s saying, put it in the variable ‘sensorValue’”
“Before you begin ANYTHING, make sure you’re sending any info from the sensor to the computer at 9600bps”
“Repeat the following commands:
  Read in the value from the analogInPin (pin A0) and save it into the variable ‘sensorValue’
  Send the variable ‘sensorValue’ over to the computer via the ‘Serial’ … = perform a calculation on the ‘sensorValue’ and use the calculated value to light up a neopixels strip
  Wait 100ms before repeating
“
Arduino code
const int analogInPin = A0;
int sensorValue = 0;
void setup() {
Serial.begin(9600);
}
void loop() {
sensorValue = analogRead(analogInPin);
Serial.println(sensorValue);
…
delay(100);
}
We can actually write out own Arduino code and make it do whatever we want, so long as we:
  Have a ‘sensor’ component
  +/- having an ‘effector’ component
Other available sensors we have here are:
  ECG
  Thermister
  EMG
  GSR
Other sensors (that need code written) include
  Accelerometer
  Polar heart rate monitor

## Slide 10: What Arduino code can do
The Vivid project (collaboration between RAMUS and University of Sydney SoMs – lead by Prof. Philip Poronnik) used an Arduino to power a few of its components
I also accidentally fried that Arduino because I had no idea what I was doing
Image source: https://www.ramus.com.au/work/many-hands-make-light-work/

## Slide 11: 3. CoolTerm – recording serial inputs
‘SensorValue’ was sent through the Serial – the particular serial it was sent through is the Universal Serial Bus (USB port)
  To use the data, we need to record this data!
Steps:
  Get a laptop from the back and open ‘CoolTerm’
    Open start menu
    Type in ‘software center’
    Run CoolTerm
    OR
  Download CoolTerm onto your own computer at http://freeware.the-meiers.org
  If nothing seems to be working…
    Options > port > COM-X (test COMs until it works…)

## Slide 12: 4. Recording serial data on CoolTerm
To record data:
  Click ‘connect’
  Connection > Capture to Textfile > Start
  Name the text file [SID].txt and save it on your desktop
To stop recording data:
  Connection > Capture to Textfile > Stop
The text file you captured will have a series of numbers on a different line – this is the raw sensor data
  Question: what range does your raw sensor data appear to fall between?

## Slide 13: 5. Graphing your data in excel
(Let’s do it in person)
Tasks to complete before you leave – collect data in a single recording session:
  1 minute resting as a baseline
  1 minute with physical activity (Squats, running on spot)
  1 minute resting for recovery
  Repeat 3 times (if time permits)
Graph your results in excel

## Slide 14: End of workshop

## Slide 15: Appendix 1: Understanding the Arduino
5V:
Used to power components FROM the arduino
GND:
Used as a NEGATIVE terminal for powered components
A0, A1, A2, A3, A4, A5:
Analogue ‘pins’ for sending and receiving DATA from Arduino components
0 – 13 (Digital):
Digital ‘pins’ for sending and receiving DATA from Arduino components

## Slide 16: Appendix 2: How does a breadboard work
Note: Arduino is upside down compared to previous image
When the 5V Pin is connected to the “positive rail”, the whole vertical rail is now connected to the 5V pin
Electricity conducts on the breadboard from one pin to ANY other pin in this horizontal rail – this means you can connect the 5V to any of the pins and it’ll still work

## Slide 17: Appendix 2: How does a breadboard work – the BUS STRIPS
Note: Arduino is upside down compared to previous image
When the GND pin is connected to the NEGATIVE rail, similarly the negative rail is COMPLETELY grounded
Again, due to the underlying design of the breadboard, you can connect the ground to ANY PIN on the negative rail and it’ll still work

## Slide 18: Appendix 2: How does a breadboard work – the BUS STRIPS
Note: Arduino is upside down compared to previous image
The two halves of the breadboard are NOT electrically connected
The positive rail on the LHS isn’t connected to the positive rail on the RHS and vice versa
Columns ABCDE aren’t connected to FGHIJ either

## Slide 19: Appendix 2: How does a breadboard work – the TERMINAL STRIPS
Note: Arduino is upside down compared to previous image
For each of the middle rows, they are electrically connected horizontally
i.e. if pin A0 is connected to row 9, effectively ALL pins in row 9 are connected to A0
Obviously remember: columns ABCDE aren’t connected to columns FGHIJ

## Slide 20: Appendix 2: How does a breadboard work – the TERMINAL STRIPS
Note: Arduino is upside down compared to previous image
For each of the middle rows, they are electrically connected horizontally
i.e. if pin A0 is connected to row 9, effectively ALL pins in row 9 are connected to A0
Obviously remember: columns ABCDE aren’t connected to columns FGHIJ

## Slide 21: Appendix 2: How does a breadboard work – connecting COMPONENTS
Note: Arduino is upside down compared to previous image
GND on the component ALWAYS connects to the negative terminal
+5V on the component ALWAYS connects to the positive terminal
The Din (Data in) pin ALWAYS connects (via a horizonal terminal) to a data (Analog or Digital) pin